## Slide 1: Sheet pile
Kratos and probabilistic library
Naam Achternaam

## Slide 2: Overview
Sheet pile model, stages
Linear model:
  Variables
  Uncertainty analysis (max displacement x)
  Uncertainty analysis (max bending moment)
Mohr-Coulomb model:
  Variables
  Uncertainty analysis (max displacement x)
  Uncertainty analysis (max bending moment)

## Slide 3: Sheet pile model, stages
Sand (3)
sand
sand
sand
Stage 0
Stage 1
Stage 2
Stage 3
Sand (3)
Sand (3)
Caly (1)
Clay (1)
Caly (2)
Clay (2)

## Slide 4: Lineair model

## Slide 5: Variables
Variable | Distribution type | Parameters
Young modulus (clay) | Uniform | 5x10**6 – 8x10**6
Young modulus (sand) | Uniform | 30x10**6 – 50x10**6
Interface stiffness | Deterministic | 10**11
Sheet pile: Young modulus | Deterministic | 200x10**9
Sheet pile: Poisson ratio | Deterministic | 0
Sheet pile: thickness | Deterministic | 0.02159
Input:
Output: total displacement x (maaiveld node), max bending moment

## Slide 6: Uncertainty analysis (total displacement x)
Stage 0 (no sheet pile)
Monte Carlo, 50 – 100 samples

## Slide 7: Uncertainty analysis (total displacement x)
Stage 1 (with sheet pile)
Monte Carlo, 50 – 100 samples

## Slide 8: Uncertainty analysis (total displacement x)
Stage 2 (excavation, no anker)
Monte Carlo, 50 – 100 samples

## Slide 9: Uncertainty analysis (total displacement x)
Stage 3 (excavation, with anker)
Monte Carlo, 50 – 100 samples

## Slide 10: Uncertainty analysis (max bending moment)
Stage 0 (no sheet pile)
Monte Carlo, 50 – 100 samples
No results returned, but there was no sheet pile

## Slide 11: Uncertainty analysis (max bending moment)
Stage 1 (with sheet pile)
Monte Carlo, 50 – 100 samples

## Slide 12: Uncertainty analysis (max bending moment)
Stage 2 (excavation, no anker)
Monte Carlo, 50 – 100 samples

## Slide 13: Uncertainty analysis (max bending moment)
Stage 3 (excavation, with anker)
Monte Carlo, 50 – 100 samples

## Slide 14: Mohr-Coulomb model

## Slide 15: Variables
Variable | Distribution type | Parameters
Cohesion | Log-normal | Mu = 3, CoV = 0.2
Friction angle (clay) | Log-normal | Mu = 22.5, CoV = 0.08
Friction angle (sand) | Log-normal | Mu = 32.5, CoV = 0.08
Young modulus (clay) | Uniform | 5x10**6 – 8x10**6
Young modulus (sand) | Uniform | 30x10**6 – 50x10**6
Sheet pile: Young modulus | Deterministic | 200x10**9
Sheet pile: Poisson ratio | Deterministic | 0
Sheet pile: thickness | Deterministic | 0.02159
Interfaces (cohesion, friction angle) | The same as soil | The same as soil
Input:
Output: total displacement x (maaiveld node), max bending moment

## Slide 16: Uncertainty analysis (max total displacement)
Stage 0 (no sheet pile)
Stage 1 (with sheet pile)
Stage 2 (excavation, no anker)
Monte Carlo, 10 - 50 samples

## Slide 17: Uncertainty analysis (max total displacement)
Stage 3 (excavation, with anker)
Monte Carlo, 10 - 50 samples

## Slide 18: Uncertainty analysis (max bending moment)
Stage 0 (no sheet pile)
Monte Carlo, 10 – 50 samples
No results returned, but there was no sheet pile

## Slide 19: Uncertainty analysis (max bending moment)
Stage 1 (with sheet pile)
Monte Carlo, 10 – 50 samples

## Slide 20: Uncertainty analysis (max bending moment)
Stage 2 (excavation, no anker)
Monte Carlo, 10 – 50 samples

## Slide 21: Uncertainty analysis (max bending moment)
Stage 3 (excavation, with anker)
Monte Carlo, 10 – 50 samples

## Slide 22: Summary

## Slide 23: Verbeterpunten
Lineair model:
  Interfaces aanpassen in het lineair model (normal, 10**11)
  Klei: Volume gewicht + young modulus
  Totale displacement, op het maaiveld ter plaatse van de damwand (met teken)  maaiveld node 171
  Onder + 2 net boven  zand
  Correlatie
Mohr-Coloumb:
  Klei: Volume gewicht + young modulus
  Totale displacement, op het maaiveld ter plaatse van de damwand (met teken)  maaiveld node 171
  Onder + 2 net boven  zand
  Interfaces: net als bij grond
  Correlatie